## Slide 1
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
Presented by
Rajshahi University of Engineering & Technology
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 2
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
Outlines
Motivation Behind the Work
Literature Review
Objectives
Mathematical Model
Graphical User Interface
SolidWorks Modeling and Simulink Simulation
Experimental Model
Future Work
Conclusion
1
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 3
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
Motivation behind the Work
Increased Accuracy
Higher Quality
Improved Working Environment
Increased Profitability
Longer Working Hour
Fig.1: Industrial Robots used in Asia by 2017 [1]
[1] IMFBlog, online: https://blogs.imf.org/2018/08/29/chart-of-the-week-invest-in-robots-and-people-in-asia/, last access: 12/8/2019
2
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 4
Literature Review
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
11/29/2019
3
Mohammed and Sunar [2]
  Forward Kinematic Model with D-H Parameter Table
  Inverse Kinematics Model with Trigonometric Approach
[2] A. A. Mohammed, M. Sunar, “Kinematics modeling of a 4-DOF robotic arm”, IEEE International Conference on Control, Automation and Robotics, May 2015.
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 5
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
Literature Review
Cekus and Posiadala [3]
  SolidWorks Model
  Kinematic Model with D-H Forward Kinematic Approach
  MATLAB SimMechanics Link Simulation
[3] D. Cekus, B. Posiadala and P. Warys, “Integration of Modeling in SolidWorks and MatLab/simulink Environments” in Archive of Mechanical Engineering, 2014.
4
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 6
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
Literature Review
Joy [4]
  3 DoF Experimental Model
  Color Sorting Ability
[4] A. Joy, “Object sorting robotic arm based on colour sensing”, International Journal of Advanced Research in Electrical, Electronics and Instrumentation Engineering, Vol. 3, March 2014.
5
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 7
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
Objectives
To establish a mathematical model of a robotic arm and do a mechanical design for the arm
To provide a perfect simulation model
To build the experimental model and interface with color sensor
To establish the gripper operation
6
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 8
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
Robotic Manipulator
Robotic Manipulator or Arm is one kind of mechanical body, usually programmable, which performs the same or similar function to human arm.
Categories of Industrial Robotic Arms:
  Cartesian Robot
  Cylindrical Manipulator
  Articulated Manipulator
  Spherical Manipulator
  Selective Compliance Articulated
  Robotic Arm (SCARA)
Fig.2: Articulated Manipulator.
7
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 9
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
Forward Kinematics
  D-H Frame Rule
    Z axis must be the axis of revolution or direction of motion
    X axis must be perpendicular to Z axis of the frame before it
    X axis must intersect Z axis of the frame before it
    Y axis must be drawn so the whole frame follows right hand rule
Mathematical Model
8
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 10
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
D-H Table |  |  |  | 
No of Frames n | Joint Angle | Angle of Twist | Length of Link | Link Offset
1 | 90+ | 90 |  | 
2 |  | 0 |  | 0
3 | 90+ | -90 | 0 | 0
D-H Table |  |  |  | 
No of Frames n |  |  |  | 
1 |  | 90 |  | 
2 |  | 0 |  | 0
3 |  | -90 | 0 | 0
Fig.3: Kinematic Scheme of the Robotic Arm
Table 1: D-H Parameter Table
Kinematic Scheme and D-H Parameter Table
9
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 11
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
Position and Rotation of the End Effector with respect to the Base Frame
Forward Kinematics Results
10
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 12
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
Simulation Model
10
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 13
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
Graphical User Interface
Fig.6: Robotic arm output with initial slider position
Fig.7: Robotic arm in 3D plotting
13
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 14
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
Experimental Model: Components
Fig.10: Arduino Mega 2560.
Operating Voltage: 5V
Digital I/O pin: 54
Analog Input Pins: 16
DC Current per I/O pin: 40mA
DC Current for 3.3V pin: 50mA
Arduino MEGA 2560
17
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 15
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
Experimental Model: Components
TCS230 Color Sensor
Power: 2.7V to 5.5V
Photodiode
Array
Current to Frequency Converter
Light
Fig.11: Functional block diagram of the color sensor
Fig.11: TCS 230 color sensor
18
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 16
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
Experimental Model: Components
Servo Motors
  Tower Pro MG 995
Gear Type: Metal gear
Operating voltage: 4.8~ 6.6V
Current draw at idle: 10mA
No load operating current draw: 170mA
Fig.12: MG 995 servo motor
19
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 17
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
Experimental Model: Components
Servo Motors
  Micro Servo SG 90
Fig.13: SG 90 Servo motor
Power supply: 3 - 6 V
Current consumption: 550 mA
20
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 18
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
Experimental Model
Fig.14: Experimental Model of the Robotic Arm
21
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 19
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
Future Scope
Following modifications can be done for further development
  Image Sensor
  Stainless Steel Bar
  Conveyor Belt
23
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 20
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
Conclusion
Mathematical Modeling has been done.
Mechanical Drawing has been simulated using SimMechanics Link.
Experimental Model has been built.
24
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 21
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
Thank You
25
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 22
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
Scopes of Work
Brick Sorter
Vegetable Separator According to Color
Separation Avoider of Medicines in Pharmaceutical Industries
Plastic Sorter by Color
Chocolate Packaging Assistance
27
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 23: HT MATRIX
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
28
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 24: HT MATRIX
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
29
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 25: MATRIX CALCULATION
Modeling of a 5R Robotic Manipulating System with 5DoF using GUI MatLab Simulation
30
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh

## Slide 26
Modeling and Development of a 3 DoF Color Sorting Robotic Manipulator using Arduino
Reference of Mathematical Modeling
[2] A. A. Mohammed, M. Sunar, “Kinematics modeling of a 4-DOF robotic arm”, IEEE International Conference on Control, Automation and Robotics, May 2015.
33
4th International Conference on Mechanical, Industrial and Material Engineering (ICMIME), 17-19 December 2019, Rajshahi, Bangladesh